## Slide 1: Permaculture design in Fire-prone landscapes
Steve Burns
April 2012
Notes: <number>

## Slide 2: Everyone is an expert – NO!
Bushfires are emotive.
Media focus on the most extreme images and stories and talk about the houses burned, not the houses saved.
Many people – city and country – perpetuate myths based on anecdote, not science.
Fire behaviour is consistent and predictable, although underlying variables may not be (e.g. exact timing of wind changes)
Notes: <number>

## Slide 3
Most of the advice in this presentation is from
The Complete Australian Bushfire Safety Book by Joan Webster
    Penguin, 1986 and subsequent editions
All students are encouraged to buy their own copy and follow Joan’s advice. Joan also has a website – you can buy direct from her.
Notes: <number>

## Slide 4: Understanding fire
“Know your enemy”
The fire triangle: three essential requirements are needed for a fire to light or stay alight
Heat
Fuel
Oxygen
Notes: <number>

## Slide 5: Fire behaviour variables
Many variables impact on the behaviour of a specific fire, including vegetation, temperature, wind direction, wind speed, relative humidity, atmospheric instability, topography and slope.
Action question:
How many of these can you control?
How many of these can you impact?
Notes: <number>

## Slide 6: Fire behaviour variables
You can change EVERY one of the variables!
You ability to change some is admittedly minor, but local changes are possible so consider how you can work on each of them.
E.g. high impact possible in terms of vegetation by changing local plantings
…while only low impact possible in terms of overall wind direction, well placed windbreaks can have local impact.
Notes: <number>

## Slide 7: Impact of slope
Speed of fire front doubles for each 10o of uphill slope and halves for each 10o of downhill slope
Are you safer uphill or downhill?
If a fire front was travelling at 10 kph and hits a 30o upslope, how fast will it move?
Notes: <number>

## Slide 8: Is your place fireprone?
Notes: <number>

## Slide 9: Historical patterns
Black Thursday 1851
Black Tuesday 1898 Roughly 44 year
Black Friday 1939 cycle
Ash Wednesday 1983
Black Saturday 2009
In Victoria, less severe events in mid & late 20’s, 1943-4 and 1967-8. [Ref: Webster (1986)]
Notes: <number>

## Slide 10: Future trends?
CSIRO modelling finds that by 2020 (relative to 1990) the annual average number of days with “Extreme” fire rating increases by 5-25% for low rate of climate change. For high rate of climate change, increase is 15-65%.
By 2050, 10-50% for low and 100-300% for high climate change rate.
(Bushfires Royal Commission submission.002.031.0385 p 10)
Notes: <number>

## Slide 11: Local patterns
Action question:
Thinking about your place or the place you’d like to live, what are fire-relevant local patterns that would impact your designs?
- Localised wind movements (gully, ridge)
- Adjacent fuel (forest, suburbs, wetland)
- Neighbours plantings or activities (native or exotic species, sheep or gorse in paddocks)
Notes: <number>

## Slide 12: Why be concerned?
Notes: <number>

## Slide 13: Killer factors
Radiant heat: intense, concentrated heat spread radially from a source [death through heat stroke as body cooling fails]
Dehydration: fluid output greater than input [death through kidney failure, following confusion, irritability, nauseau & sleepiness]
Asphyxiation: 1) super-heated air swells throat, compresses windpipe 2) fine particles in smoke clog airways until unable to breathe [NOT lack of oxygen]
Notes: <number>

## Slide 14: Quick myth busters re asphyxiation
Oxygen is NOT sucked out of the air (if it was, the fire would go out!). Extreme fires use huge amounts of oxygen but more rushes into the area (this is how big fires create their own weather)
Carbon monoxide CAN be given off in fires, but isn’t an issue in open air bushfires as it is lighter than air and rises rapidly
Steam from super-heated hose water CAN burn air passages, so you need a mask
Notes: <number>

## Slide 15: Design strategies
Sector planning & property layout
  Layout design tips
Passive defense:
  Location of buildings
  Design of buildings (inc refuges/bunkers)
Active defense:
  Emergency plans
  firefighting
Notes: <number>

## Slide 16: Sector planning & property layout
Identify fire risk sector in initial planning
Property layout:
  Bare ground/cut grass/driveway
  Bodies of water
  Vegetable garden
  Radiant heat shields (brick wall, garage)
  Fire and wind breaks
  Fruit trees/evergreens/fire retardant species
  Distance to forest or flammable vegetation
Notes: <number>

## Slide 17: Layout design tips
Determine a Zone 0 & 1 area of protection, with home as centre, to provide a haven for people, pets & possessions.
Include stock in the area of protection, if possible.
Design protection from advancing fire front, radiant heat and ember attack.
Focus on fireward side, but plan for wind changes and slow leeward advance
Notes: <number>

## Slide 18: Layout design tips- windbreaks
Windbreaks should be 3-5 rows ‘thick’ and include under-storey plantings to stop increased velocity as wind squeezes under lower branches of the break
Windbreaks reduce wind velocity for a distance of 5-10 x height in front and 15-30 x height on the lee
Windbreaks increase soil moisture up to 20% for as much as 25 x their height
Dense windbreaks give best protection for buildings, people and stock; permeable windbreaks give best protection for crops
Notes: <number>

## Slide 19: Layout design tips
Radiant heat shields include low hedges, earth mounds and solid walls.
Sheds, garages and workshops should be leeward of the house and well away in case flammable contents explode.
Water supply must be within protection zone. Multiple water sources critical. Plastic pipes at least 400 mm underground.
Stock refuge yards: windbreaks on 2 sides, ploughed ground firebreaks 6 m wide, contain water source, accommodate all stock
Notes: <number>

## Slide 20: Layout design tips
Firewood should be stacked in enclosed shed 20 m+ to the lee of the house with leeward opening door.
Never stack wood under trees
Run main driveway (4 m+ wide) along contour, without sharp bends or dips, but with passing bays at 200m intervals if very long. Encircle house with driveway loop or provide turning circle of at least 12.5 m for large fire vehicles.
Remove flammable vegetation from against walls or flammable fences.
Notes: <number>

## Slide 21: Vegetation design tips
Species lists are available online – including Australian lists which identify suitable native species.
Plants with broad, fleshy leaves or high salt content burn less readily than those with fine hard leaves
The volatile oils in eucalypts (gums and tea tree) make them particularly dangerous
Plant form is also relevant – open or closed, low to ground or upright, smooth bark not rough bark
Notes: <number>

## Slide 22: Optimum distances
Open country/farmland > 10 m of cleared land between property and flammable crops/grass
Homes near bushland > 30-100 m of cleared ground under trees
Homes near dense bush > up to 300 m between buildings and bush
Homes on hillsides, ridges of tumultuous terrain >
200-300 m litter clearing in all directions
Major firebreaks in all directions, not just fireward side
Notes: <number>

## Slide 23: Defensive strategies
House location
Fire danger increases with:
  Orientation to firewinds
  Steep slopes
  Distance up a hillside or embankment
  Ruggedness of landscape
  Closeness to dense bushland
continued…/
Notes: <number>

## Slide 24: House location danger factors
  Exposure to large areas of dry grass or crop
  Lack of non-combustible barriers
  Density of flammable vegetation retained on site
  Narrow dead-end roads
  Smallness of site, long narrow site
  Lack of water
  Density of housing
Notes: <number>

## Slide 25: House design
A bushfire-resistant design needs to
deflect winds
keep out sparks
discourage wind-whirls
screen from radiated heat
be strengthened against wind uplift
e.g. simple, squat design on flat land or set into slope
Notes: <number>

## Slide 26: House design summary
Keeping sparks and embers out is the priority
Many fires start in the roof space which gets very hot (air 50o +) & full of super-heated dust
External cladding is not very important (consistent research from 1939 onwards)
Window protection is important: shutters or metal flywire (now mandatory)
Notes: <number>

## Slide 27: House design
Foundations: concrete slab eliminates risk of sub-floor ignition. Raised sub-floors should be brick, concrete or stone (metal can weaken & collapse under sustained radiant heat)
Utilities run through floor space means no gaps in cavity walls through which sparks could enter.
Exterior wall design uncluttered to reduce wind eddies.
Posts in post and beam construction (e.g. mud brick houses) should be enclosed
Wall cavities should be insulated
Notes: <number>

## Slide 28: House design
Insulation: should meet “4 Zero” rating standard – it will not catch fire, spread flame, build up heat or develop smoke
Vents and cracks should be covered with metal flywire or filled with a fire-resistant gap mastic/silicon
Fascias, barges and eaves are safest when metal
Downpipes of metal are better than plastic
Decks: timber catches sparks and can light from below. If possible, use paving, brick or cement
Notes: <number>

## Slide 29: House design
Exterior doors should be solid core with minimum 30 minute fire rating. Fit draught strips all around to stop ember entrance. Fit full all-metal flyscreen door. Pet holes must be sealable with metal covers.
Interior doors should be draught-proofed to close off individual rooms and restrict fire advance
Chimneys and fireplaces need internal dampers, spark arresters and bronze flywire on chimney top.
Fireplaces need tight-fitting metal screen across face.
Notes: <number>

## Slide 30: House design
Windows: if timber, paint & keep smooth. Metal frames can warp but won’t burn. Sills safest if brick or masonry and well sloped.
Window glass can shatter in intense heat, no matter its material strength. (toughened laminated glass shattered on Ash Wednesday). External fly screens on all window faces (inc non-opening) will protect from sparks not debris or radiant heat. Shutters will protect from all.
Do not fit skylights in fire-prone areas.
Notes: <number>

## Slide 31
Notes: <number>

## Slide 32: House design
Meter box should be metal
External wall cupboard on leeward side of house to contain firefighting equipment
Furnishings can char and die out (wool, leather) or burst into flames (cotton, linen, some synthetic materials). Consider both covering material and padding.
Sprinkler systems can be cheap (sacrificial plastic) or very expensive (copper). Pumps can’t rely on mains.
Houses don’t explode!
Notes: <number>

## Slide 33: Bunker or refuge room?
Bunker is an external refuge
Refuge room is within the house
Neither are designed for long-term occupancy. The only ‘approved’ bunker is approved for one hour.
Webster discourages bunkers but encourages a safe refuge room within the house. Alternative to evacuation for children or elderly who cannot defend and place of retreat for defenders as fire front hits.
“It is not the answer to bushfire safety, but the answer to the evacuation paradox” (Webster p 121)
Notes: <number>

## Slide 34: Refuge room
Refuge room should have:
  Strong construction of low flammability materials
  A water supply, preferably a permanent reserve water supply with hose permanently attached to reserve tap
  Small window, reinforced with wire mesh or fitted with internally operated shutter
  Means of viewing fire progress (window or spyglass)
  Outer door leading to non-flammable cleared area with radiant heat shields
Notes: <number>

## Slide 35: Refuge room
Refuge room should have:
  Inner & outer doors either solid core timber or insulated and reinforced with layer of heavy cement sheet between two timber layers
  Ceiling of concrete, or timber ceiling joists lined above and below with double layered ‘fire stop’ plaster with 100 mm square mesh reinforcing attached to joists
  Concrete floor or timber floor insulated from below
  Manhole in ceiling if roof is directly above
Notes: <number>

## Slide 36: Bunker
Bunker is an external, underground shelter, best located to the leeward side of the house.
(In the 1939 fires, some timber mill workers survived in crude dug outs with timber roofs)
Bunkers should NOT be furnished or have windows.
Ventilation must avoid draughts, smoke and spark entry
A normal cellar is NOT a safe bushfire retreat (flooring collapse into cellar would kill occupants). An existing cellar could be reinforced with a concrete ceiling.
Notes: <number>

## Slide 37: Bunker features
Concrete or other material to ensure long term structural integrity (not timber & corrugated iron)
Clear of trees or structures which could fall on it
Door protected from radiant heat on multiple sides
Possible connection to the house via sheltered path
Commercial bunkers are now available…
Notes: <number>

## Slide 38
6 person, one hour rating - $6,990 in 2011
Notes: <number>

## Slide 39: Active defense
Stay or go?
If you evacuate, how often do you do it – and where do you go?
If you stay, how do you defend your property?
See CFA FireReady Kit – free online
PLAN & REHEARSE your plans
Notes: <number>

## Slide 40
Notes: <number>

## Slide 41: Does defending work?
House defended by… survival rate
No-one 30%
Passersby/neighbours 44%
One householder 82%
One or more 10 yrs old+ 90%
3- 4 people 100%
[Mt Macedon fires, 1983. Melbourne University and National Centre for Rural Fire Research]
Notes: <number>

## Slide 42: Personal survival kit
Clothes
Thick wool blanket (big enough to cover you)
Goggles (side protection + demisting vents)
Bottle of artificial tears
Smoke mask or Water for damping face cover
UV cream, zinc cream or reflective skin cream
First aid kit
Have a survival kit for each family member
Notes: <number>

## Slide 43: Clothing
Cover whole body (head, face, back of neck)
Comfortable, loose-fitting – NOT tight
Wool is best – fire retardant and insulating.
Cotton will burn but thick cotton OK
Strong hat able to be tied on (due to winds)
Pure wool or cotton balaclava
Boots with heat resistant soles (no hobnails or steelcaps which can burn feet)
Strong non-plastic gloves
Notes: <number>

## Slide 44: Fighting a fire
Needs people and water … should be part of a plan and well prepared for…
Assume all utilities will be cut off.
Have (multiple) reserve water supplies – preferably gravity fed
Sprinkler systems need 22 – 25,000 litres reserve; may need to run system for three hours from first ember attack
Pumps: diesel better at high temperature
Buckets should be metal & two per station
Notes: <number>

## Slide 45: Have a written plan
CFA research shows 75% of people in high bushfire risk areas don’t have a written plan.
Anticipate a range of scenarios and brainstorm with friends and family (remember pets/stock)
Even if your plan is to evacuate every time, you might one day be unable to do so – what is your Plan B?
cfa.gov.vic.au
Notes: <number>